## Slide 1
QORVO_RADIO2
Industry Supporters: Jed Sander | David Kegley | Nathan Whitt | Daisy Vazquez | Faculty Mentors: Prof. Nabila (Nan) BouSaba | Dr. Fareena Saqib
Team Members: Luke Matthews [lmatth23@charlotte.edu] | Kenneth Le [kle26@charlotte.edu] | Abdul Bah [abah2@charlotte.edu] | Alberto Hernandez [aherna86@charlotte.edu] | Ethan Hartman [ehartma6@charlotte.edu]
Senior Design I - Fall 2025
Objective
Design, develop, and replicate a device with multiple protocols and peripherals.
Can communicate through a mesh network to promote RF research at UNCC.
Requirements
Two or more unique Protocols
Three or more unique peripherals
2.4GHz - 2.5GHz ISM Band
3”x3”x3” enclosure
0.5 lbs
QPG6200L SoC
Battery life greater than week
IoT Block Diagram
Implementation Plan (SDII)
Remeasure extrusions and manufacture enclosure. (1/12/2026)
Assemble the initial replicated PCB to design specifications. (1/19/2026)
Program initial replicated remote devices. (1/26/2026)
Conduct rigorous testing to verify compliance with operational specifications. (3/1/2026)
Deliver fully functional remote devices that communicate through mesh network. (4/24/2026)
Future Usage (After SDII)
Serve as an interactive educational tool to promote RF research
at UNC Charlotte and Qorvo’s
technological advancements.
GitHub
Budget
$3,250 Total Budget
$1,891.24 Spent
$74.44 Per Device
CAD Model
Mechanical Enclosure Design
PCB
Peripherals Selected
PDM 🗣️🎙️
SPI 🔊
Analog🚪🔔
UART 🕺
Protocols Selected
Why these Peripherals
PDM will capture voice via a digital MEMS microphone
SPI will drive a speaker and amplifier for audio playback
Analog detects push button presses to trigger doorbell events
UART interfaces with an ultrasonic sensor for motion detection and alerts
Start
Send a command
Uses BLE?
Speaker & Mic receives GATT command
Output Speaker Audio
Movement Detector senses motion
Doorbell receives GATT command
Trigger chime event
Gateway receives status & sends it to tablet
Update tablet with device responses
Lighting System receives On/Off cluster command
Activate
LED lights
Yes
Activate lights?
No
Send light signal
No
Yes
Transmit audio?
No
Yes
Gateway receives command through Wi-Fi AP/direct connection
Convert to Zigbee format & send
Convert to BLE format & send
Main SoC
PCB Schematic
Side View
Top View
End